## Slide 1: IEEE 802.11 Overview Mustafa Ergen ergen@eecs.berkeley.edu UC Berkeley

## Slide 2: Wireless Market Segments

## Slide 3: Standardization of Wireless Networks
Wireless networks are standardized by IEEE.
Under 802 LAN MAN standards committee.
Application
Presentation
Session
Transport
Network
Data Link
Physical
ISO
OSI
7-layer
model
Logical Link Control
Medium Access (MAC)
Physical (PHY)
IEEE 802
standards
Notes: Same organization that came up with IEEE 802.3 Ethernet,
which is responsible for success of Internet

## Slide 4: IEEE 802.11 Overview
Adopted in 1997.
Defines;
MAC sublayer
MAC management protocols and services
Physical (PHY) layers
  IR
  FHSS
  DSSS
Goals
To deliver services in wired networks
To achieve high throughput
To achieve highly reliable data delivery
To achieve continuous network connection.

## Slide 5: Components
Station
BSS - Basic Service Set
  IBSS : Infrastructure BSS : QBSS
ESS - Extended Service Set
  A set of infrastrucute BSSs.
  Connection of APs
  Tracking of mobility
DS – Distribution System
  AP communicates with another

## Slide 6: Services
Station services:
  authentication,
  de-authentication,
  privacy,
  delivery of data
Distribution Services ( A thin layer between MAC and LLC sublayer)
  association
  disassociation
  reassociation
  distribution
  Integration
A station maintain two variables:
authentication state (=> 1)
association state (<= 1)

## Slide 7: Ex.

## Slide 8: Medium Access Control
Functionality;
Reliable data delivery
Fairly control access
Protection of data
Deals;
Noisy and unreliable medium
Frame exchange protocol - ACK
Overhead to IEEE 802.3 -
Hidden Node Problem – RTS/CTS
Participation of all stations
Reaction to every frame

## Slide 9: MAC
Retry Counters
  Short retry counter
  Long retry counter
  Lifetime timer
Basic Access Mechanism
  CSMA/CA
  Binary exponential back-off
  NAV – Network Allocation Vector
Timing Intervals: SIFS, Slot Time, PIFS, DIFS, EIFS
DCF Operation
PCF Operation

## Slide 10: DCF Operation

## Slide 11: PCF Operation
Poll – eliminates contention
PC – Point Coordinator
  Polling List
  Over DCF
  PIFS
CFP – Contention Free Period
  Alternate with DCF
Periodic Beacon – contains length of CFP
CF-Poll – Contention Free Poll
NAV prevents during CFP
CF-End – resets NAV

## Slide 12: Frame Types
Protocol Version
Frame Type and Sub Type
To DS and From DS
More Fragments
Retry
Power Management
More Data
WEP
Order
FC
Duration
/ID
Address
1
Address
2
Address
3
Sequence
Control
Address
4
DATA
FCS
2 2 6 6 6 2 6 0-2312 4 bytes
NAV information
Or
Short Id for PS-Poll
BSSID –BSS Identifier
TA - Transmitter
RA - Receiver
SA - Source
DA - Destination
IEEE 48 bit address
Individual/Group
Universal/Local
46 bit address
MSDU
Sequence Number
Fragment Number
CCIT CRC-32 Polynomial
Upper layer data
2048 byte max
256 upper layer header

## Slide 13: Frame Subtypes
RTS
CTS
ACK
PS-Poll
CF-End & CF-End ACK
Data
Data+CF-ACK
Data+CF-Poll
Data+CF-ACK+CF-Poll
Null Function
CF-ACK (nodata)
CF-Poll (nodata)
CF-ACK+CF+Poll
Beacon
Probe Request & Response
Authentication
Deauthentication
Association Request & Response
Reassociation Request & Response
Disassociation
Announcement Traffic Indication Message (ATIM)
CONTROL
DATA
MANAGEMENT

## Slide 14: Other MAC Operations
Fragmentation
  Sequence control field
  In burst
  Medium is reserved
  NAV is updated by ACK
Privacy
  WEP bit set when encrypted.
  Only the frame body.
  Medium is reserved
  NAV is updated by ACK
  Symmetric variable key
WEP Details
  Two mechanism
    Default keys
    Key mapping
  WEP header and trailer
    KEYID in header
    ICV in trailer
  dot11UndecryptableCount
    Indicates an attack.
  dot11ICVErrorCount
    Attack to determine a key is in progress.

## Slide 15: MAC Management
Interference by users that have no concept of data communication. Ex: Microwave
Interference by other WLANs
Security of data
Mobility
Power Management

## Slide 16: Authentication
Authentication
  Prove identity to another station.
  Open system authentication
  Shared key authentication
    A sends
    B responds with a text
    A encrypt and send back
    B decrypts and returns an authentication management frame.
  May authenticate any number of station.
Security Problem
  A rogue AP
    SSID of ESS
    Announce its presence with beaconing
    A active rogue reach higher layer data if unencrypted.

## Slide 17: Association
Association
  Transparent mobility
  After authentication
  Association request to an AP
  After established, forward data
  To BSS, if DA is in the BSS.
  To DS, if DA is outside the BSS.
  To AP, if DA is in another BSS.
  To “portal”, if DC is outside the ESS.
  Portal : transfer point : track mobility. (AP, bridge, or router) transfer 802.1h
  New AP after reassociation, communicates with the old AP.

## Slide 18: Address Filtering
More than one WLAN
Three Addresses
Receiver examine the DA, BSSID
Privacy MAC Function
WEP Mechanism

## Slide 19: Power Management
Independent BSS
  Distributed
  Data frame handshake
  Wake up every beacon.
  Awake a period of ATIM after each beacon.
  Send ACK if receive ATIM frame & awake until the end of next ATIM.
  Estimate the power saving station, and delay until the next ATIM.
  Multicast frame : No ACK : optional
Overhead
  Sender
    Announcement frame
    Buffer
    Power consumption in ATIM
  Receiver
    Awake for every Beacon and ATIM

## Slide 20: Power Management
Infrastructure BSS
  Centralized in the AP.
  Greater power saving
  Mobile Station sleeps for a number of beacon periods.
  Awake for multicast indicated in DTIM in Beacon.
  AP buffer, indicate in TIM
  Mobile requests by PS-Poll

## Slide 21: Synchronization
Timer Synchronization in an Infrastructure BSS
  Beacon contains TSF
  Station updates its with the TSF in beacon.
Timer Synchronization in an IBSS
  Distributed. Starter of the BSS send TSF zero and increments.
  Each Station sends a Beacon
  Station updates if the TSF is bigger.
  Small number of stations: the fastest timer value
  Large number of stations: slower timer value due to collision.
Synchronization with Frequency Hopping PHY Layers
  Changes in a frequency hopping PHY layer occurs periodically (the dwell meriod).
  Change to new channel when the TSF timer value, modulo the dwell period, is zero

## Slide 22: Scanning & Joining
Scanning
  Passive Scanning : only listens for Beacon and get info of the BSS. Power is saved.
  Active Scanning: transmit and elicit response from APs. If IBSS, last station that transmitted beacon responds. Time is saved.
Joining a BSS
  Syncronization in TSF and frequency : Adopt PHY parameters : The BSSID : WEP : Beacon Period : DTIM

## Slide 23: Combining Management Tools
Combine Power Saving Periods with Scanning
  Instead of entering power saving mode, perform active scanning.
  Gather information about its environments.
Preauthentication
  Scans and initiate an authentication
  Reduces the time

## Slide 24: The Physical Layer
    PLCP: frame exchange between the MAC and PHY
    PMD: uses signal carrier and spread spectrum modulation to transmit data frames over the media.
  Direct Sequence Spread Spectrum (DSSS) PHY
    2.4 GHz : RF : 1 – 2 Mbps
  The Frequency Hopping Spread Spectrum (FHSS) PHY
    110KHz deviation : RF : PMD controls channel hopping : 2 Mbps
  Infrared (IR) PHY
    Indoor : IR : 1 and 2 Mbps
  The OFDM PHY – IEEE 802.11a
    5.0 GHz : 6-54 Mbps :
  High Rate DSSS PHY – IEEE 802.11b
    2.4 GHz : 5.5 Mbps – 11 Mbps :

## Slide 25: IEEE 802.11E
  EDCF - Enhanced DCF
  HCF - Hybrid Coordination Function
  QBSS
  HC – Hybrid Controller
  TC – Traffic Categories
  TXOP – Transmission Opportunity
    – granted by EDCF-TXOP or HC- poll TXOP
  AIFS – Arbitration Interframe Space

## Slide 26: IEEE 802.11E

## Slide 27: IEEE 802.11E Backoff

## Slide 28: IEEE 802.11 Protocols
  IEEE 802.11a
    PHY Standard : 8 channels : 54 Mbps : Products are available.
  IEEE 802.11b
    PHY Standard : 3 channels : 11 Mbps : Products are available.
  IEEE 802.11d
    MAC Standard : operate in variable power levels : ongoing
  IEEE 802.11e
    MAC Standard : QoS support : Second half of 2002.
  IEEE 802.11f
    Inter-Access Point Protocol : 2nd half 2002
  IEEE 802.11g
    PHY Standard: 3 channels : OFDM and PBCC : 2nd half 2002
  IEEE 802.11h
    Supplementary MAC Standard: TPC and DFS : 2nd half 2002
  IEEE 802.11i
    Supplementary MAC Standard: Alternative WEP : 2nd half 2002

## Slide 29: APPENDIX

## Slide 30: The Basics of WLANs

## Slide 31: WLAN Pending Issues
Why 802.11a?
  Greater bandwidth (54Mb)
  Less potential interference (5GHz)
  More non-overlapping channels
Why 802.11b?
  Widely available
  Greater range, lower power needs
Why 802.11g?
  Faster than 802.11b (24Mb vs 11Mb)

## Slide 32: Deployment Issues
  Re-purpose Symbol AP’s for secure admin services
  Deploy 802.11b with 802.11a in mind (25db SNR for all service areas)
  Delay migration to 802.11a until dual function (11b & 11a) cards become available

## Slide 33: Frequency Bands- ISM
Extremely
Low
Very
Low
Low
Medium
High
Very
High
Ultra
High
Super
High
Infrared
Visible
Light
Ultra-
violet
X-Rays
Audio
AM Broadcast
Short Wave Radio
FM Broadcast
Television
Infrared wireless LAN
902 - 928 MHz
26 MHz
Cellular (840MHz)
NPCS (1.9GHz)
2.4 - 2.4835 GHz
83.5 MHz
(IEEE 802.11)
5 GHz
(IEEE 802.11)
HyperLAN
HyperLAN2
Industrial, Scientific, and Medical (ISM) bands
Unlicensed, 22 MHz channel bandwidth

## Slide 34: IEEE 802.11i Enhanced Security
Description | Enhancements to the 802.11 MAC standard to increase the security; addresses new encryption methods and upper layer authentication
Importance | High: weakness of WEP encryption is damaging the 802.11 standard perception in the market
Related standards | This applies to 802.11b, 802.11a and 802.11g systems. 802.1x is key reference for upper layer authentication
Status + Roadmap | Enhanced encryption software will replace WEP software; This is on a recommended best practice /voluntary basis; development in TgI: first draft Mar 2001; next draft due Mar 2002; stable draft: July 2002; final standard: Jan 2003
Products affected | Client and AP cards (Controller chip, Firmware, Driver) AP kernel, RG kernel, BG kernel
Agere’s activity | Actively proposing WEP improvement methods, participating in all official/interim meetings
Key players | Agere/Microsoft/Agere/Cisco/Atheros/Intel/3Com/Intersil/Symbol/Certicom/RSA/Funk
Key issues | Mode of AES to use for encryption (CTR/CBC [CBC MIC] or OCB [MIC and Encryption function])

## Slide 35: IEEE 802.1X - Port Based Control
Description | A framework for regulating access control of client stations to a network via the use of extensible authentication methods
Importance | High: forms a key part of the important 802.11i proposals for enhanced security
Related standards | This applies to 802.11b, 802.11a and 802.11g systems
Status + Roadmap | Standard available – Spring 2001
Products affected | Supported in AP-2000, AP-1000/500, Clients (MS drivers for XP/2000 beta)
Agere’s activity | Adding EAP auth types to products
Key players | Microsoft/Cisco/Certicom/RSA/Funk
Key issues | Home in IETF for EAP method discussions

## Slide 36: IEEE 802.1p - Traffic Class
Reference | IEEE 802.1p (Traffic Class and Dynamic Multicast Filtering)
Description | A method to differentiate traffic streams in priotity classes in support of quality of service offering
Importance | Medium: forms a key part of the 802.11e proposals for QoS at the MAC level
Related standards | This applies to 802.11b, 802.11a and 802.11g systems; is an addition to the 802.1d Bridge standard (annex H).
Status + Roadmap | Final standard; incorporated in 1998 edition of 802.1d (annex H)
Products affected | Client and AP cards (Driver); AP kernel, RG kernel, BG kernel
Agere’s activity | Investigating implementation options
Key players | N/A
Key issues | N/A

## Slide 37: Glossary of 802.11 Wireless Terms, cont.
BSSID & ESSID: Data fields identifying a stations BSS & ESS.
Clear Channel Assessment (CCA): A station function used to determine when it is OK to transmit.
Association: A function that maps a station to an Access Point.
MAC Service Data Unit (MSDU): Data Frame passed between user & MAC.
MAC Protocol Data Unit (MPDU): Data Frame passed between MAC & PHY.
PLCP Packet (PLCP_PDU): Data Packet passed from PHY to PHY over the Wireless Medium.

## Slide 38: Overview, 802.11 Architecture
STA
STA
STA
STA
STA
STA
STA
STA
AP
AP
ESS
BSS
BSS
BSS
BSS
Existing Wired LAN
Infrastructure Network
Ad Hoc Network
Ad Hoc Network

## Slide 39: Frequency Hopping and Direct Sequence Spread Spectrum Techniques
Spread Spectrum used to avoid interference from licensed and other non-licensed users, and from noise, e.g., microwave ovens
Frequency Hopping (FHSS)
  Using one of 78 hop sequences, hop to a new 1MHz channel (out of the total of 79 channels) at least every 400milliseconds
    Requires hop acquisition and synchronization
    Hops away from interference
Direct Sequence (DSSS)
  Using one of 11 overlapping channels, multiply the data by an 11-bit number to spread the 1M-symbol/sec data over 11MHz
    Requires RF linearity over 11MHz
    Spreading yields processing gain at receiver
    Less immune to interference

## Slide 40: 802.11 Physical Layer
Preamble Sync, 16-bit Start Frame Delimiter, PLCP Header including 16-bit Header CRC, MPDU, 32-bit CRC
FHSS
  2 & 4GFSK
  Data Whitening for Bias Suppression
    32/33 bit stuffing and block inversion
    7-bit LFSR scrambler
  80-bit Preamble Sync pattern
  32-bit Header
DSSS
  DBPSK & DQPSK
  Data Scrambling using 8-bit LFSR
  128-bit Preamble Sync pattern
  48-bit Header

## Slide 41: 802.11 Physical Layer, cont.
Antenna Diversity
  Multipath fading a signal can inhibit reception
  Multiple antennas can significantly minimize
  Spacial Separation of Orthoganality
  Choose Antenna during Preamble Sync pattern
    Presence of Preamble Sync pattern
    Presence of energy
      RSSI - Received Signal Strength Indication
    Combination of both
Clear Channel Assessment
  Require reliable indication that channel is in use to defer transmission
  Use same mechanisms as for Antenna Diversity
  Use NAV information

## Slide 42: Performance, Theoretical Maximum Throughput
Throughput numbers in Mbits/sec:
  Assumes 100ms beacon interval, RTS, CTS used, no collision
  Slide courtesy of Matt Fischer, AMD